## Slide 1: PERSONAL PROTECTIVE EQUIPMENT
SAFETY TRAINING MODULE
Notes: <number>

## Slide 2: Federal OSHA Standard Overview
Applies to general industry
Governs the use, selection, maintenance, fit and disposal of Personal Protective Equipment
Employers are to assess hazards in their workplace and select appropriate PPE
<number>
Notes: The federal Occupational Safety and Health Administration
(OSHA) issued a revised Personal Protective Equipment (PPE) standard in 1994. OSHA‘s revised standard became
effective on 7/5/94, with the exception of the Hazard
Assessment and Employee Training requirements
which became effective 90 days later.
This regulation applies to the use, selection, maintenance,
fit and disposal of PPE. It also requires employers to
assess existing job hazards in their workplace and select the
proper type of PPE for workers to use that will provide one additional barrier against job injuries.
OSHA makes it clear that PPE is not a substitute for
engineering, administrative or work practice controls,
but an additional control to be used in conjunction with
others, to present a barrier against specific workplace
hazards. Each of you needs to be aware that this equipment
does not eliminate the hazard. If the equipment fails, the
exposure and possibility of injury remain.

## Slide 3: OSHA Standard General Requirements
Employers to select PPE based on hazards present or likely to be present
Prohibits use of defective / damaged equipment
Requires training employees in PPE use, fit, maintenance, life expectancy & disposal
<number>
Notes: The general requirements of this standard require each employer
to select appropriate PPE based on the hazards that are present
or are likely to be present in the workplace.
The employer is to provide the necessary equipment
and take measures so as to prohibit the use of damaged or
defective equipment.
The employer is also to take the role of training employees
in the proper use, fit, maintenance, life expectancy and
disposal of PPE. Workers are to be trained to recognize
and understand the potential hazards within the workplace
and how to correctly use the PPE provided to them and that’s
our purpose today. However, please understand that the
PPE that may be assigned to each of you does not eliminate
the hazard and can only protect you if it is used and maintained
as it was designed to do.

## Slide 4: Hazard Assessment
Employers required to conduct a workplace hazard assessment
Employees exposed to identified hazards are to be provided with appropriate PPE
Employers are to certify in writing that the hazard assessment has been completed
Damaged or defective PPE is not to be used
<number>
Notes: Employers are further required to assess the workplace to determine
if hazards that require the use of PPE are present or are likely
to be present. If so, the employer must select and have affected
employees use properly fitted PPE designed to protect the
workers from the identified hazards.
The requirement states that employers must certify in writing
that a workplace hazard assessment has been performed.
Once the assessment is completed, PPE has been provided, and
workers trained in it’s use, then the employer and workers
must work together to ensure that defective or damaged PPE is
not used and is replaced as necessary.
Discuss the results of an actual workplace hazard assessment
that has been conducted or outline future plans to do so.
TRANSITION: Now that we’ve discussed the hazard assessment
and PPE selection steps, let’s review what training is to be provided
to workers...

## Slide 5: Training
Employees to be instructed when PPE is necessary, what type, how to wear it, limitations, proper care, maintenance, useful life, and disposal
Employers are to certify that training has been completed and that employees understand it
<number>
Notes: Employees are to trained before doing work that requires the
use of PPE. This training is to consist of knowing when to
wear the equipment, what type is necessary, how it is to be
worn, and what it’s limitations are. In addition, the proper
care, maintenance, useful life and disposal procedures are
to be discussed. We will be covering this information today.
Employers are required to certify in writing that training
has been completed and that employees understand the
training. Therefore, we ask that none of you leave here today
without a clear understanding of the use and care of PPE
that may be assigned to you.

## Slide 6: OSHA Standard General Requirements
TYPES OF PPE:
Clothing, equipment, respiratory devices, protective shields and barriers
Protect eyes, face, head, torso and extremities
Process hazards, environment, chemicals, radiological, or mechanical hazards
Capable of causing injury or impairment through absorption, inhalation, or physical contact
<number>
Notes: The types of PPE referenced in this standard include clothing,
respiratory devices, protective shields and barriers.
This PPE is designed to protect the eyes, face, head, torso and
extremities from hazards in the workplace.
These hazards may be process hazards and they may be
environmental, chemical, radiological, or mechanical in nature.
These hazards can result in bodily injury through the processes
of absorption (being absorbed through the skin), inhalation (being
inhaled into the lungs) or through other means of physical contact.
Let’s discuss the various types of PPE...

## Slide 7: Types of PPE
Eye & Face Protection
Hearing Protection
Respiratory Protection
Head Protection
Arm & Hand Protection
Foot & Leg Protection
Torso Protection
<number>
Notes: The OSHA standard primarily deals with these types of protection.
The American National Standards Institute (ANSI) has published
performance standards that manufacturers must meet in designing,
manufacturing, and testing many of these types of equipment. The
ANSI label or tag on equipment indicates that this design standard
has been met and assures product quality.
Briefly touch on each type listed above.
TRANSITION: Let’s discuss each major type of PPE, one by one...
Instructor’s Note: The next 7 slides cover each of the items listed
above in more detail. Be sure to discuss and demonstrate the actual
equipment that is applicable to your workplace. Demonstrate the
proper care and fitness adjustments with each piece of equipment
shown.

## Slide 8: Eye & Face Protection
Protect from flying particles, molten metal, liquid chemicals, acids, caustic liquids, chemical gases or vapors, and light radiation
Sideshield protection needed for flying particles
Use safety prescription lenses or eye protection worn over regular glasses or contacts
Protection needed to cover multiple hazards
<number>
Notes: Eye and face equipment is designed to protect the body from
flying particles, molten metal, liquid chemicals, acids, caustic
liquids, chemical gases or vapors, and light radiation.
Safety glasses used to protect against flying particles are required
to be equipped with sideshields. Additional protection needs to
be worn over non-safety prescription lenses and contacts.
Incidentally, OSHA does not consider contact lenses to be a form
of eye protection, but neither does it consider contacts to be
detrimental to the wearer’s safety and health.
Protection is to be taken against multiple hazards. An example
is a welder that may be exposed to both flying particles and
light radiation. Protection must be provided against both hazards
and not just the more severe hazard.
Equipment to protect the eyes and face come in a wide variety of
types and styles including certain hard hats equipped with
face shields.

## Slide 9: Hearing Protection
Required in high noise areas, depending on the duration of worker exposure
Long term exposure can result in permanent hearing loss or impairment
Improperly worn or maintained PPE will not sufficiently reduce the noise levels
PPE - earplugs or earmuffs
<number>
Notes: Hearing loss usually happens gradually over a period of time so that the worker may not even realize the extent of the loss until it is too late. Hearing loss that occurs in this fashion is usually permanent and irreversible.
Hearing needs to be protected when noise levels reach or exceed 85 decibels (measured on the A scale) for an 8 hour exposure time.
Short bursts of noise that exceed even higher decibel levels can also require hearing protection as a control measure.
As protection, earplugs generally offer the most protection. Foam earplugs that fit snugly are the most effective. To insert properly, roll the earplug into a small diameter, place it well into the ear canal, and insert. It may help to pull your ear back and up as you insert the plug.
After you have inserted it, hold the plug in your ear for a few seconds to ensure a good fit.
Earmuffs fit over the outside of your ear. Their effectiveness is limited by the seal they form around the ear. Facial hair, earrings, and eyeglasses can all compromise the effectiveness of this seal. The sponge material that forms the seal also needs to be in good condition with no cracks or leaks.

## Slide 10: Respiratory Protection
Two Basic Types
  Air Purifying Respirators
  Atmosphere Supplying Respirators
<number>
Notes: The revised PPE standard did not change the existing respiratory
protective equipment standard. However, let’s take a few minutes
to review this standard so that we’re all aware of the requirements.
The two basic types of respirators are the air purifying type and
the atmosphere supplying type.
Air purifying respirators use filters or sorbents to remove harmful
substances from the air. They include simple disposal masks
and range to sophisticated filtering devices. This equipment does
not supply oxygen and is not to be used in oxygen deficient or
other harmful atmospheres.
Atmosphere supplying respirators are designed to provide
breathable air from a clean air source. The two types of
atmosphere supplying respirators are the self-contained
breathing apparatus and the supplied air respirator.

## Slide 11: Head Protection
Overhead hazards
Exposed electrical conductors
Helmets rated as Types 1 or 2 and providing Class A, B or C protection A = General impact, 2200 volts protection B = 20,000 volts protection C = Bump protection, no electrical protection
<number>
Notes: Head protection is to be provided to protect against overhead
falling hazards or exposed electrical conductors that could contact
the head.
For industrial purposes, three classes of protective head devices
are recognized: Class A is the typical hard hat worn by construction
workers which provides general impact protection and electrical
protection up to 2,200 volts.
Class B helmets are specifically designed to protect from high
voltage electrical hazards and are rated to provide protection up
to 22,000 volts.
Class C helmets are lightweight and designed to provide bump
protection only. Electrical contact is not anticipated since these
helmets are typically constructed of aluminum, an excellent
conductor of electricity. They are typically used in oil fields,
refineries and chemical plants.
You should be able to identify the type of helmet you’re using by
looking inside the shell for the manufacturer’s name, ANSI designation,
and class rating.

## Slide 12: Arm & Hand Protection
Hazards from chemicals and other substances, temperature extremes, sharp objects
Injuries include cuts, abrasions, burns, amputations, shock, chemical absorption
Glove protection information to be obtained from the manufacturer
Protection includes gloves, sleeves, hand pads, wristlets, etc.
Rubber insulating equipment needed for electrical workers
<number>
Notes: Hand protection is necessary when there is exposure to
hazardous chemicals or other substances, severe cuts and
lacerations, severe abrasions, punctures, chemical burns, and
temperature extremes.
Keep in mind that no glove is resistant to all chemicals. Using a
glove designed to resist one chemical may be totally inappropriate
to use with another chemical. Manufacturers data should be referred
to if in doubt of the specific resistance qualities of a glove.
Rubber protective equipment for electrical workers must conform
to the the requirements established by ANSI.
The type of glove selected should fit the requirements and hazards
associated with the particular job. Glove selection should include:
  the toxic properties of the chemicals use.
  the work being performed including the degree of dexterity
  needed as well as the duration, frequency, and degree of
  chemical exposures.
  the performance characteristics of the gloves, such as
  resistance to chemicals, punctures, tears, and abrasions.

## Slide 13: Foot & Leg Protection
Hazards from falling or rolling objects, objects piercing the sole, electrical hazards, molten metal, hot surfaces, slippery surfaces
Shoes / boots may provide impact protection, compression protection, puncture protection
Leggings protect the lower legs and feet from molten metal and welding sparks
<number>
Notes: Foot protection is to be provided where hazards are encountered
that expose the feet to rolling hazards (such as roll paper or
coil steel), objects capable of piercing the sole (such as heavy
gauge metal staples), or where feet are exposed to electrical hazards.
Shoes or boots are available that provide impact protection,
compression protection and puncture protection. Safety shoes
should be sturdy and provide an impact-resistant toe. In some
shoes, metal soles protect against sole puncture. Additional protection,
such as metatarsal guards is also available. Safety shoes come in a
wide variety of styles and materials.
ANSI standards specify the requirements and testing procedures
and specifications associated with compression and impact tests.
Leggings protect the lower leg and feet against exposure to molten
metal and welding sparks. Safety snaps provide the wearer
a means of rapid removal of the leggings.

## Slide 14: Torso Protection
Hazards include heat, splashes from liquids, impacts, cuts, and radiation
Injuries include heat burns, radiation burns, and chemical burns, lacerations, and abrasions
Equipment includes vests, jackets, aprons coveralls, and full body suits.
<number>
Notes: As with our discussion about chemically-resistant gloves, make sure that the torso protection provided is specifically manufactured to resist the particular chemical or other hazardous substance that you are working with. Mixing of equipment within different operations is not condoned.

## Slide 15: Care, Use, Maintenance, & Disposal of PPE
PPE is available in various types and styles
Make sure that the PPE assigned to you fits properly and snugly
Clean PPE regularly, following manufacturer’s suggestions
Be familiar with the life expectancy of your PPE and dispose of when needed
Report any discomfort, problems or questions to your supervisor or safety manager
<number>
Notes: Review each of these points with the workers.
Equipment should fit the individual worker and should be reasonably comfortable. The equipment should not be altered or modified by the worker or it’s effectiveness may be compromised.
Equipment should be kept clean by the individual worker. Follow manufacturer s instructions. Cleaning PPE is important for sanitary reasons and is usually easily accomplished. For example, cleaning of hard hat shells can be done by dipping them for at least one minute in hot water, approximately 140 degrees F, that contains a mild detergent. Shells can be scrubbed and then rinsed in clear hot water. After rinsing, shells can be inspected for cracks or other signs of damage.
Daily inspection of PPE by the worker of assigned PPE ensures that no unfit equipment is being used. A supply of new PPE should be established so that replacement is immediate.

## Slide 16: Personal Protective Equipment
Final Discussion
Question and Answer Period
<number>
Notes: Lead a final discussion on key points covered and again remind workers that PPE does not eliminate the hazard, it only provides one additional barrier of protection.
Ask for any final questions and thank all for attending.